## Slide 1
Smart Parking.
Team:
Davide Marchetti / 815990
Mattia Vincenzi / 860579
Laboratorio IoT / Prof. Paolo Napoletano
A.A. 2020 / 2021

## Slide 2: Prototype.

## Slide 3: Materials (hardware).
Name | Quantity
ESP 8266 | 6
ESP 32 (Master) | 1
Ultrasonic sensor (HC-SR04) | 1
Pir motion sensor (HC-SR501) | 1
Lettore RFID (MFRC 522) | 1
Photoresistor | 1
LEDs (red, green, blu and white) | 9
Servo motor | 2
Buzzer | 1
Push button | 1
Display 16x2 | 1
Resistors | 14

## Slide 4: Materials (software).
Name
Visual Studio Code (C++)
Mosquitto MQTT broker
MySQL
InfluxDB
HTML + TailwindCSS + Vue.js
Web Socket
Telegram
OpenWeather

## Slide 5: Architecture.

## Slide 6: MQTT (1/3).
Every sensor will auto-configure itself after each boot with JSON payloads exchanged though MQTT.
Master will always wait for configuration requests on a defined topic.
Configuration mechanism
Send a configuration request for the current subsystem type.
Request the configuration from MySQL.
Obtain and customize the configuration for the specific device (mac_address).
Reply to the requester with the final configuration.
EXTERNAL DISPLAY
LIGHT SYSTEM
PARKING SENSOR
2
3
1
4
MASTER

## Slide 7: MQTT (2/3).
Given its configuration, each subsystem knows which topic to publish on and will collect data regularly.
Data publishing mechanism
Send a JSON payload with the raw data.
If necessary, data are processed (mean over a defined time amount) and published on InfluxDB.
EXTERNAL DISPLAY
LIGHT SYSTEM
PARKING SENSOR
MASTER
5
6
2
3
1
4

## Slide 8: MQTT (3/3).
A last will message will be delivered on its own topic when the connection to the subsystem is lost or upon a device failure.
EXTERNAL DISPLAY
LIGHT SYSTEM
PARKING SENSOR
2
3
1
4
MASTER

## Slide 9: How it works.

## Slide 10: Roof and OpenWeather API.

## Slide 11: Gate, Deep Sleep and EEPROM.

## Slide 12: Lights.

## Slide 13: Alarm.

## Slide 14: Car Park.

## Slide 15: Telegram bot.

## Slide 16: Last Will.

## Slide 17: Dashboard.
Developed with TailwindCSS and Vue.js

## Slide 18: MySQL.
Configuration Examples
Recorded Events
Recorded Devices

## Slide 19: InfluxDB.

## Slide 20: Final Remarks.